## Slide 1
Project 59
Interactive Social Guide Robot
Decision making using a rule-based and an LLM-integrated navigation pipeline
Background
A guide robot must recognise interest in interaction while roaming the laboratory. Changing gaze and distance, and missed detections, make this decision difficult.
Objective
Develop a temporal social-state pipeline for Navel to support a comparison and evaluation of rule-based and LLM decisions in navigation scenarios
How can gaze and distance observations over time be structured into a shared social-state representation for rule-based and LLM decision-making?
Conclusion and future work
By Eddie Kim and Jeruh Kim
Contact: hkim807@aucklanduni.ac.nz jkim828@aucklanduni.ac.nz
Supervisor: Ho Seok Ahn
RQ1
How well can an LLM’s decisions align with human preferences and appropriateness ratings, compared with those of a rule-based policy using the same representation?
RQ2
Navel Sensors
Track History
Shared Social State
A structured summary of the social context and available evidence
Decision Policies
Rule-based and LLM policies select an action from the same social state
Person detections, social cues and robot movement data
Person histories, changes in attention and distance, and observation quality
APPROACH
Interested person
farther away
Move closer
ENGAGE
Interested person
already nearby
Stop and greet
Hello!
YIELD
Person needs
room to pass
Give room to pass
CONTINUE
No sustained
interest in interaction
Stay on the route
Four possible actions
Method
Results
Behaviour comparison across eight scenarios
Description (Human) | Survey preference (action and %) | Rule-based | LLM
Passes without looking | CONTINUE (83.3%) | [Action] | [Action]
Beside route, sustained gaze | APPROACH (45.2%) | [Action] | [Action]
Already nearby, sustained gaze | YIELD (42.9%) | [Action] | [Action]
Approaches on route, no gaze | YIELD (90.5%) | [Action] | [Action]
Walks away without looking | CONTINUE (57.1%) | [Action] | [Action]
Passes with a brief glance | CONTINUE (73.8%) | [Action] | [Action]
Beside route, intermittent gaze | APPROACH (50.0%) | [Action] | [Action]
Walks away while looking | ENGAGE (61.9%) | [Action] | [Action]
Agreement with survey preference
Rule-based [X]/8 LLM [Y]/8
N = 42 · Eight selected scenarios · Same decision point
Chart: Mean decision latency (s)
| Rule-based | LLM
Mean decision latency (s) | 1.3 | 5.8
Rule-based [mean] s · LLM [mean] s
Same recorded inputs and hardware.
Decision request to returned action.
[Runs] repetitions; LLM: [model].
Notes: Draft poster for Project 59. Students: Eddie Kim and Jeruh Kim. Supervisor: Ho Seok Ahn. Contact: hkim807@aucklanduni.ac.nz.
Sources: /Users/eddiekim/Downloads/Poster Design Guide.pdf (A1 portrait, required fields, PDF <50 MB). Its 2024 deadline is historical. /Users/eddiekim/Downloads/Speech_Nilushika2023.pdf. Layout reference: /Users/eddiekim/Downloads/Poster_77 (1).pdf.
Survey source: /Users/eddiekim/Downloads/Human Evaluation of Robot Behaviour (Responses).xlsx, Form responses 1. Preference counts and all 36 rating means independently verified against config/human-reference.json. Every preference bar sums to 37. Unable to judge is a survey response, not an action.
Pipeline source: docs/results/first-action-live-output/results.csv, report.md, verification.json. Nine SDK captures, first valid policy output, identical initial eligible states. qwen2.5:7b, temperature 0, seed 42, warmed model. Times are from replay start, not inference latency. All actions NOT_EXECUTED_OFFLINE.
Both policies produce outputs in S2,S3,S9. Six no-action cases remain in coverage denominator. LLM outputs fail live-client acceptance (S2 stale observation, S3 gaze not ready, S9 person no longer visible). Acceptance/timings reflect one development replay and may vary.
The survey clips are trimmed and trim offsets are unavailable. This prevents survey-end human-alignment scoring. Initial survey is completed. Human evaluation of actual completed-system behaviour is future work. Do not claim VLM/hybrid results or policy superiority.
Navel product image: https://navelrobotics.com/wp-content/uploads/2025/02/Navel0157-scaled.jpg via https://navelrobotics.com/en/navel-the-new-empathy-robot-for-good-care/. University logo extracted unchanged from supplied exemplar. Official department logo is a labelled draft field. No sponsor confirmed.
Fonts Rubik and Noto Sans are design selections evoking the robot, not verified official brand fonts.