## Slide 1
Project 59
Interactive Social
Guide Robot
Decision-making with shared social evidence
A robot on a laboratory route must decide
when to interact and when to make space.
CONTINUE
APPROACH
ENGAGE
YIELD
PHOTO PLACEHOLDER: LAB PHOTO
Eddie Kim and Jeruh Kim
Notes: Presentation time: 35 seconds.
Introduce the team. Navel follows a fixed route in a laboratory and must select one of four social-navigation actions. Changing gaze, distance and missing detections make single observations insufficient. Our objective is an integrated temporal representation and a fair comparison of rule-based and LLM decisions.
Sources:
/Users/eddiekim/Downloads/Poster_59.pptx
/Users/eddiekim/Documents/Projects/P4P/docs/llm-refinement-summary.md

## Slide 2
Research Questions and Evaluation
Project 59
2
RQ1
How can gaze and distance over time become
shared evidence for both decision policies?
RQ2
How do their decisions compare with human
preferences and appropriateness ratings?
Human video judgments
Laboratory sensor recordings
Paired policy evaluation
Preferred action and
appropriateness ratings
Nine controlled scenarios
using real Navel observations
First eligible action
and time to complete output
Current scores describe expected first actions in tuning recordings. Survey-endpoint alignment remains separate.
Notes: Presentation time: 40 seconds.
RQ1 asks how gaze and distance observations over time can be structured into a shared social state. RQ2 asks about alignment with human preferences and appropriateness ratings. The survey judges the immediate action at a video endpoint. The latest tuning study instead scores the first eligible action. Do not equate its 9/9 and 8/9 benchmark scores with survey-endpoint human accuracy. The available verified historical reference has 37 responses, while a 42-response update is unverified. Main slides therefore omit a participant count.
Sources:
/Users/eddiekim/Downloads/Poster_59.pptx
/Users/eddiekim/Documents/Projects/P4P/config/human-reference.json
/Users/eddiekim/Documents/Projects/P4P/docs/pipeline-refinement.md
/Users/eddiekim/Documents/Projects/P4P/config/final-scenarios.json

## Slide 3
Shared Temporal Social-State Pipeline
Project 59
3
Navel sensors
Gaze, distance, motion
HTTP receiver
Validate and record
Track history
Time and evidence quality
Full SocialState
Diagnostic record
DecisionState
Shared compact input
Rule policy
LLM policy
Selected action
Output and freshness checks
Robot action
Opt-in handler
Current gaze
Looking history
Relative separation
Validity and position
Both policies share measured evidence. Unknown cues remain explicit. Physical execution is opt-in.
Notes: Presentation time: 60 seconds.
Sensors stream person detections, gaze, distance, nose geometry and robot motion through HTTP. The server maintains histories and derives temporal cues and validity. Full SocialState retains diagnostics. Both policies receive the same compact DecisionState. A selected policy produces action and reason. Trial correlation, readiness and freshness govern delivery. Native execution is opt-in. Continuous rule commands use a separate target-lock flow, detailed in the appendix. The reported replay trials instantiate no robot executor.
Sources:
/Users/eddiekim/Documents/Projects/P4P/docs/architecture.md
/Users/eddiekim/Documents/Projects/P4P/app/state/decision_models.py
/Users/eddiekim/Documents/Projects/P4P/robot/navel_client/single_trial.py
/Users/eddiekim/Documents/Projects/P4P/docs/target-lock.md

## Slide 4
Rule-Based Decision Policy
Project 59
4
Observed evidence | Action
Sustained looking, farther away | APPROACH
Sustained looking, already nearby | ENGAGE
Closing inside corridor, low looking | YIELD
Other eligible cases | CONTINUE
Refinements
Temporal gaze and gap handling
Distance-aware thresholds
Corridor and closing evidence
9/9
expected first actions
Notes: Presentation time: 40 seconds.
The initial design used gaze and proximity conditions. Refinements calibrated distance-dependent gaze thresholds, kept time and missing-data boundaries, and added forward-corridor plus closing evidence to the low-gaze YIELD condition. The final preset disables recurring intermittent attention as an interaction trigger. These are simplified examples, not the full precedence. The final rule matches all nine expected first actions on this tuning set.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/policy/rules.py
/Users/eddiekim/Documents/Projects/P4P/config/temporal-final-scenarios.json
/Users/eddiekim/Documents/Projects/P4P/docs/social-policy.md

## Slide 5
Compact Evidence Improved LLM Performance
Project 59
5
First decision | Initial | Final selection
Expected-action agreement | 6/9 | 8/9
Median output delay | 6.21s | 3.20s
Median input tokens | 1,766 | 917
What we retained
Compact shared evidence
Descriptive labels and clear instructions
Qwen 2.5 7B
DecisionState v3
Instructions v16
Delay starts at the first eligible observation. Richer labels did not improve the 8/9 score.
Notes: Presentation time: 45 seconds.
The initial LLM received the full SocialState including configuration, raw geometry and unused diagnostics. Compact projection was the largest improvement: 6/9 to 8/9 and 6.21 seconds to 2.76 seconds in stage 3. Current semantic descriptions and the v16 instructions retain 8/9, with the latest fresh model control median 3.20 seconds. Stage 3 is the faster historical reference, and richer labels have no demonstrated accuracy gain. Timings are warm local runs, not randomized causal estimates. The final selection is Qwen 2.5 7B, DecisionState v3 and v16.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-1-2/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-3/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-4/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-5/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/REPORT.md

## Slide 6
First-Action Accuracy and Decision Delay
Project 59
6
Chart: 
| Rules | Selected LLM
Value | 9 | 8
Expected first actions matched
S4 SCENARIO PHOTO
Insert the closing encounter inside the forward corridor
Same S4 evidence | First action
Rules | YIELD
Selected LLM | CONTINUE
LLM median 3.20s
Three repetitions on nine tuning recordings. LLM 95th percentile: 6.34s after eligibility.
Notes: Presentation time: 50 seconds.
Both policies use identical evidence. Rules match 9/9 expected first actions; Qwen 2.5 7B matches 8/9 in all three repetitions. The LLM median is 3.20 seconds after eligibility, with 95th percentile 6.34 seconds. Median motion-to-output is 4.31 seconds in these recordings. S4 remains wrong: the same in-corridor, closing, low-gaze evidence leads rules to YIELD and the LLM to CONTINUE. Current scores use nine tuning recordings, not held-out human alignment. Readiness and freshness checks can reject a syntactically valid output.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/JUDGEMENT-REVIEW.md

## Slide 7
Robot Behaviour Demonstration
Project 59
7
VIDEO PLACEHOLDER
15-second montage: route following, approach, greeting and giving space
Shared evidence made comparison possible
Compact input improved LLM decisions and delay.
The tuned rule policy remained more reliable on tested first decisions.
Notes: Presentation time: 30 seconds.
Play approximately 15 seconds of the prepared montage, then deliver the closing contribution. Use captions that distinguish scripted action execution from autonomous policy selection. Four short shots can show route progress, approach, greeting and giving space. These action demonstrations do not turn recorded inference results into measured physical execution rates. Closing: We developed a shared temporal social-state pipeline and a repeatable way to compare decision quality and delivery time. Compact input substantially improved the LLM, while the tuned rules remained more reliable on tested first decisions.
Sources:
/Users/eddiekim/Documents/Projects/P4P/docs/robot-decision-dry-run.md
/Users/eddiekim/Documents/Projects/P4P/docs/physical-executor.md

## Slide 8
Appendix: Technical Details and Evidence
Appendix 01
8
Topic | Slides
Evaluation and human reference | 9 to 11
Sensors, history and cue calculations | 12 to 18
Rule policy and target locking | 19 to 23
Shared input and LLM instructions | 24 to 26 and 36
Refinement results and model comparison | 27 to 32 and 35
Final configuration and research limits | 33 to 34
Tables, figures and diagrams are editable. Photo and video frames are labelled placeholders.
Notes: Appendix for questions.
The five-minute presentation ends at slide 7. Use the following slides selectively for questions. All numerical results refer to their frozen experiment and timing origin.
Sources:

## Slide 9
Frozen First-Decision Evaluation
Appendix 02
9
Case | Allowed first actions | Rules | LLM | Eligible after motion
S1 | CONTINUE | CONTINUE | CONTINUE | 1.18s
S2 | APPROACH | APPROACH | APPROACH | 1.10s
S3 | ENGAGE / APPROACH | ENGAGE | ENGAGE | 1.21s
S4 | YIELD | YIELD | CONTINUE | 1.10s
S5 | CONTINUE | CONTINUE | CONTINUE | 1.17s
S6 | CONTINUE | CONTINUE | CONTINUE | 1.11s
S7 | CONTINUE | CONTINUE | CONTINUE | 1.71s
S8 | APPROACH / ENGAGE / CONTINUE | CONTINUE | CONTINUE | 1.17s
S9 | APPROACH | APPROACH | APPROACH | 1.14s
S8 first uses an empty scene. These expected-action labels are evaluator metadata and never enter policy input.
Notes: Appendix for questions.
Exactly nine motion-trimmed SDK recordings are the tuning set. Freeze the first eligible source snapshot and unchanged allowed-action lists. Invalid/missing first outputs count as failure. Later calls use separate frozen last-eligible points and cannot replace the first result. Three deterministic repeats are repeated measurements of the same nine scenarios. S8 resolves while the observed scene is empty; it does not demonstrate later gaze or departure recognition. S3 and S8 allow several actions.
Sources:
/Users/eddiekim/Documents/Projects/P4P/config/final-scenarios.json
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-1-2/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/REPORT.md

## Slide 10
Human Reference: Available Evidence
Appendix 03
10
Reference | Status
Historical source | 37 responses per scenario, verified
Later workbook update | 42 expected, source unavailable/unverified
Survey decision point | Immediate next action at clip end
Operational decision point | First eligible observation
Direct survey-end scoring | Clip-to-sensor mapping unverified
Historical S3 example | YIELD | ENGAGE
Preferred-action votes | 18 | 12
Mean appropriateness | 3.57 | 3.78
Human preference and mean appropriateness can disagree. Current 9/9 and 8/9 scores use expected first actions.
Notes: Appendix for questions.
The historical source reference verifies 37 responses per scenario, with independent action-rating denominators 34 to 37. A later 42-response workbook is expected but unavailable/unverified in the stored run. The historical example below deliberately demonstrates preference/rating disagreement rather than claiming current human accuracy. S3 has YIELD 18 votes and ENGAGE 12 votes, while mean appropriateness is higher for ENGAGE. Survey clip trim-to-SDK endpoint mappings are unverified, so direct RQ2 alignment remains unresolved. Replace/update the survey figure after verifying the final dataset and endpoint mapping.
Sources:
/Users/eddiekim/Documents/Projects/P4P/config/human-reference.json
/Users/eddiekim/Documents/Projects/P4P/docs/results/pipeline-refinement/reference-verification.json
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/poster-20261011-final-first-output-01/human-reference.json
/Users/eddiekim/Documents/Projects/P4P/docs/pipeline-refinement.md

## Slide 11
Metric Definitions and Timing Origins
Appendix 04
11
Measure | Definition
First-action agreement | Action belongs to the unchanged expected set
Output validity | Strict action enum and nonblank reason
Live-client acceptance | Correlation, current readiness and freshness
Eligibility to output | First eligible observation to complete observed output
Motion to output | Recorded motion onset to complete observed output
Later diagnosis | Separate frozen observation, excluded from primary score
3.20s median
6.34s 95th percentile
Timing origin: after eligibility. Recorded motion-to-output median: 4.31s.
Notes: Appendix for questions.
Action agreement means the first action belongs to the frozen allowed set. Strict validity means the parser accepts the enum and nonblank reason, not semantic correctness. Client acceptance additionally checks correlation, readiness and freshness. Time to complete observed output starts at first eligibility; motion-to-output includes the evidence wait. Components have independent medians. The latest 7B run has 3.20-second output median, 6.34-second 95th percentile, 1.17-second median eligibility after motion and 4.31-second measured motion-to-output median. These are local replay timings, excluding physical LAN and action execution.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-1-2/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/scripts/profile_llm_baseline.py

## Slide 12
Navel Sensor Inputs and Mapping
Appendix 05
12
SDK observation | Shared evidence | Interpretation
Person UID | Track identity and epoch | Bookkeeping outside LLM text
dist_mm | distance_m = dist_mm / 1000 | Measured robot-person range
gaze_overlap | Latest gaze score | Thresholded measurement
Face bounding box | face_detected | Face detection only
g_nose in CAM_HEAD | Corridor position | Fixed-head position estimate
Forward and yaw velocity | Robot motion state | Translation or rotation
Missing or invalid values | null / UNKNOWN | Unavailable evidence
HTTP POST /api/v1/observations. No measured pass gesture or path-relation input is available from Navel.
Notes: Appendix for questions.
Use actual SDK perception and latest prior locomotion packets. dist_mm is converted to metres. Raw score is gaze overlap, not interest probability. A finite positive-size face bounding box supplies face detection. Nose geometry selects finite nonzero CAM_HEAD points; never relabel another frame. Latest locomotion supplies measured forward/yaw velocities. Missing/invalid/stale values remain unavailable. Unsupported path relation/pass gesture measurements have been removed. Raw safety range units remain unverified and do not enter the compact LLM social evidence. HTTP keeps the newest pending frame, with at most ten POST starts per second by default.
Sources:
/Users/eddiekim/Documents/Projects/P4P/docs/raw-observation-frame.md
/Users/eddiekim/Documents/Projects/P4P/docs/navel-supported-cues.md
/Users/eddiekim/Documents/Projects/P4P/robot/navel_client/adapter.py

## Slide 13
Person History and Detection Continuity
Appendix 06
13
ACQUIRED
New epoch
OBSERVED
Collect samples
MISSING
Retain briefly
LOST
Remove history
Final tracking setting | Value
History window | 3.0s
Missing grace | 0.75s
Capacity | 64 samples per track, 32 tracks
Nose continuity distance | At most 0.45m
Nose continuity time | At most 0.25s, adjacent single-person frames
Same UID within grace preserves its epoch. Geometric continuity is a heuristic, not verified identity.
Notes: Appendix for questions.
Identify histories by session, SDK UID and track epoch. Missing grace 0.75 seconds is distinct from the target lock hold of two seconds. A return after expiry starts a new epoch. The final preset enables a limited nose-based cross-UID continuity heuristic only for one retained/current person in adjacent frames with finite nonzero CAM_HEAD positions, distance at most 0.45 metres and elapsed time at most 0.25 seconds. This can preserve history/epoch through SDK churn but does not prove physical identity. The separate target-lock handoff keeps a logical lock while a new raw track builds fresh history.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/state/tracks.py
/Users/eddiekim/Documents/Projects/P4P/config/person-tracking-final-scenarios.json
/Users/eddiekim/Documents/Projects/P4P/docs/person-tracking.md

## Slide 14
Current Gaze: Score to Classification
Appendix 07
14
Measured distance | Looking entry | Looking exit
At or below 2.75m | 0.93 | 0.90
Beyond 2.75m | 0.97 | 0.95
Score at or above entry
LOOKING
Score in hysteresis band
Keep previous classification
Score at or below exit
NOT LOOKING
Null or a source gap resets memory to UNKNOWN
Gaze overlap is a measured score. It does not express a probability of interest or willingness.
Notes: Appendix for questions.
gaze_thresholds uses near thresholds at distance <=2.75m and stronger thresholds at distance >2.75m. gaze >= enter sets looking true; gaze <= exit sets false; values in the band keep the previous state. An uninitialised band remains unknown. A null score, nonadjacent source frame or gap >0.25s resets sample memory. Score 0.5 is valid low gaze in this preset. The face label does not establish gaze or facing. Labels recompute from authoritative evidence.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/state/features.py
/Users/eddiekim/Documents/Projects/P4P/config/temporal-final-scenarios.json

## Slide 15
Temporal Looking: Coverage and Categories
Appendix 08
15
Looking fraction = measured looking time / covered gaze time
Evidence gate | Final value
Recent window / minimum span | 3.0s / 1.0s
Known samples / coverage | 5+ samples / 0.6s+
Coverage fraction | At least 50%
SUSTAINED entry / retention | 80% / 65% + looking
NONE entry / retention | 20% / 35%
Dwell / trailing-run minimum | 0s / 0s
S7 first observation
69.3%
Measured looking fraction
Current gaze: not looking
Category: INTERMITTENT
Trailing looking run: 0s
High recent looking fraction can coexist with a current non-looking sample. Missing time stays uncovered.
Notes: Appendix for questions.
Integrate only adjacent intervals where both sample classifications are known. The interval uses the earlier classification for looking duration. coverage sums valid durations, looking_time sums durations classified true, gaze_fraction is looking_time divided by coverage. sustained_gaze_s is the trailing contiguous true run. Count bouts only from observed false-to-true transitions; detector gaps cannot create bouts. Sufficiency requires current known gaze, at least five known samples, span >=1s, coverage >=0.6s and coverage fraction >=0.5. Sustained category needs current looking true plus fraction >=0.8 entering or >=0.65 retaining. NONE enters <=0.2 or retains <=0.35. Current preset dwell/run minimum are zero. Example S7 is measured, not illustrative.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/state/features.py
/Users/eddiekim/Documents/Projects/P4P/app/state/estimator.py
/Users/eddiekim/Documents/Projects/P4P/config/temporal-final-scenarios.json

## Slide 16
Distance Change Uses a Robust Fitted Slope
Appendix 09
16
Chart: Distance (m)
| 0 | 0.087913 | 0.174289 | 0.305376 | 0.391769 | 0.480427 | 0.567527 | 0.700715 | 0.786007 | 0.872113 | 0.999566 | 1.08583
Measured distance | 3.5238 | 3.6158 | 3.5238 | 3.4174 | 3.5238 | 3.2396 | 3.3346 | 3.2396 | 3.4332 | 3.253 | 3.1646 | 3.3346
Median-slope fit | 3.525 | 3.1849
m = median of pairwise slopes
b = median(d - m t)
S4 fit | Value
Slope | -0.313m/s
RMS residual | 0.093m
Samples / span | 12 / 1.09s
Classification | DECREASING
Actual S4 first-decision samples. Negative slope describes decreasing separation, not verified human motion.
Notes: Appendix for questions.
Fit only the newest contiguous valid-distance segment. The implementation uses a Theil-Sen-style median of all pairwise slopes, not ordinary least squares. Intercept is median(d_i - m*t_i). RMS residual measures error about this line. This figure uses actual S4 samples from the frozen first decision; reconstructed values exactly reproduce stored slope. n=12, span=1.08583s, slope=-0.3132622696787195m/s, intercept=3.5250032471403463m, RMS=0.09263065031506869m. Either participant can cause changing separation.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/state/features.py
/Users/eddiekim/Documents/Projects/P4P/config/temporal-final-scenarios.json
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/common/snapshots/S4/first.social-state.json

## Slide 17
Distance Fit Quality and Trend Labels
Appendix 10
17
Fit-quality condition | Final value
Minimum sample count | 5
Minimum segment span | 1.0s
Maximum fit samples | 32, evenly sampled when needed
Maximum source gap | 0.25s
Jump allowance | 3.0m/s times elapsed time + 0.05m
Maximum RMS residual | 0.10m
Valid fitted slope | Trend
m < -0.10m/s | DECREASING
-0.10 to +0.10m/s | STABLE
m > +0.10m/s | INCREASING
Invalid evidence | UNKNOWN
Null, gap or jump starts a new fitting segment
The model receives the category and validity. Full diagnostics retain slope, span, residual and jump counts.
Notes: Appendix for questions.
Sample adjacency requires contiguous frame_sequence and dt>0 through max_gap_s. Nulls/gaps/jumps break the fitting segment. A jump exceeds 3.0m/s * dt +0.05m and invalidates that latest distance at this update. Subsequent clean samples accumulate a new fit. Downsample evenly to at most 32 fit samples if necessary. Five samples and span at least one second are required. Fit is valid only with current observed distance and RMS <=0.1m. Trends use strict inequalities below -0.1 and above +0.1m/s; equality is STABLE.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/state/features.py
/Users/eddiekim/Documents/Projects/P4P/app/state/estimator.py
/Users/eddiekim/Documents/Projects/P4P/config/temporal-final-scenarios.json

## Slide 18
Proximity Bands and Forward-Corridor Position
Appendix 11
18
Distance band | Category
At most 0.6m | TOO_CLOSE
Above 0.6m through 2.0m | INTERACTION_RANGE
Above 2.0m through 6.0m | APPROACHABLE
Beyond 6.0m | FAR
Corridor half width 0.40m
Hysteresis 0.05m
Fixed head, offsets and yaw = 0
Chart: Lateral (m)
| 3.155548828125
S1 first | 0.63261
S4 first | 0.27337
S7 first | 0.89367
Corridor boundary | 0.4 | 0.4
Opposite boundary | -0.4 | -0.4
Nose position estimates current corridor occupancy. It does not establish collision, future clearance or intent.
Notes: Appendix for questions.
Final bands use bisect_left without zone hysteresis: <=0.6m TOO_CLOSE, (0.6,2] interaction, (2,6] approachable, >6 far. Fixed-head CAM_HEAD nose transforms into forward/lateral using configured camera offset and yaw. Current offsets and yaw are zero. Corridor half width 0.4m, hysteresis 0.05m: initial <=0.4m, retain IN_WAY to0.45m, reenter from TO_SIDE at <=0.35m. Forward <=0 is BEHIND. Missing/invalid geometry or disabled fixed-head interpretation is UNKNOWN. Positions below are actual first snapshots, not predicted trajectories. No body envelope or dynamic head compensation is modelled.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/state/path_position.py
/Users/eddiekim/Documents/Projects/P4P/config/temporal-final-scenarios.json
/Users/eddiekim/Documents/Projects/P4P/docs/path-position.md

## Slide 19
Supported Rule Precedence
Appendix 12
19
Order | Eligible evidence | Action
1 | Configured continuous empty interval complete | CONTINUE
2 | IN_WAY, valid closing, low gaze, face, within 3.5m | YIELD
3 | Same closing and low-gaze evidence, TO_SIDE | CONTINUE
4 | Held SUSTAINED category, latest gaze not looking | CONTINUE
5 | Attentive and already within conversation range | ENGAGE
6 | Reliable increasing separation outside conversation range | CONTINUE
7 | Attentive within approach distance | APPROACH
8 | Other eligible evidence | CONTINUE
Readiness precedes this table. No policy output is supplied for an unready observation.
Notes: Appendix for questions.
These are ordered supported v7 conditions. Readiness gates invocation. Current preset disables recurring attention; the general rule supports it only when enabled. YIELD additionally requires detected face, observed person, distance <=3.5m, latest looking false, valid NONE gaze and current gaze overlap <=effective exit threshold. Sustained category held with current looking false returns CONTINUE before interaction branches. IN_WAY/TO_SIDE paired closing conditions differ only by current position. No unsupported measured path or gesture branch remains.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/policy/rules.py
/Users/eddiekim/Documents/Projects/P4P/config/temporal-final-scenarios.json

## Slide 20
Rule Refinements and Final Parameter Choices
Appendix 13
20
Setting | Final value | Design purpose
Conversation / social range | 2m / 6m | Approach versus speaking nearby
Near gaze entry / exit | 0.93 / 0.90 | Classify compressed SDK scores
Far gaze entry / exit | 0.97 / 0.95 | Stronger gaze beyond 2.75m
History / minimum span | 3s / 1s | Build evidence within short encounters
Minimum gaze coverage | 0.6s and 50% | Preserve missing-data boundaries
Extra dwell / trailing run | 0s / 0s | Avoid additional decision delay
Closing YIELD range | At most 3.5m | Detect closing in the corridor
Recurring-looking trigger | Disabled | Avoid interaction after incidental looks
The preset fits these nine tuning recordings. Thresholds do not establish human interest or universal social rules.
Notes: Appendix for questions.
These are engineering choices tuned on the same nine recordings, not population-calibrated thresholds. They address compressed gaze scores, unreliable far gaze, intermittent detections, passing beside the robot and empty intervals. No independent sensor accuracy or held-out policy generalisation follows from fitting the preset. Native physical approach stopping distance is separate from a descriptive proximity band.
Sources:
/Users/eddiekim/Documents/Projects/P4P/config/temporal-final-scenarios.json
/Users/eddiekim/Documents/Projects/P4P/config/person-tracking-final-scenarios.json
/Users/eddiekim/Documents/Projects/P4P/docs/final-scenario-tuning.md

## Slide 21
Person Locking: Logical Target Lifecycle
Appendix 14
21
UNLOCKED
LOCKED
MISSING
Sole visible track
Target absent
TENTATIVE_RETURN
One new UID
AMBIGUOUS
Several candidates
COOLDOWN
Release and wait
Stable lock ID binds to a UID and track epoch
Missing, tentative or ambiguous states return HOLD with no effective action.
Tracking grace is 0.75s. The separate logical target-lock hold is 2.0s.
Notes: Appendix for questions.
The continuous rule command/head-focus flow maintains one logical lock ID bound to a session, UID and epoch. It can acquire a sole visible track even before a ready proposal, unless no-attention/receding policy dismisses it. LOCKED permits matching target actions or YIELD; other proposals can hold. A missing target preserves the logical lock for less than two seconds. Same UID/epoch returning within hold restores it. Multiple candidates cause AMBIGUOUS. New UID is TENTATIVE_RETURN and needs guarded evidence. Policy release, timeout, long stream gap, engagement completion or terminal execution failure releases to cooldown. A hold returns effective_decision null, not a fifth action. SingleTrial first-output scoring is separate from this effective command layer.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/policy/target_lock.py
/Users/eddiekim/Documents/Projects/P4P/config/target-lock.json
/Users/eddiekim/Documents/Projects/P4P/docs/target-lock.md

## Slide 22
Guarded UID Handoff and Release Values
Appendix 15
22
Lock or handoff condition | Final value
Target missing hold | 2.0s
Release cooldown | 1.0s
New UID return window | 0.8s
Candidate evidence | At least 3 frames over at least 0.15s
Candidate maximum frame gap | 0.35s
Allowed distance change | 0.25m + 1.5m/s times elapsed time
Maximum handoffs per lock | 3
Identity guard | One exclusive candidate, both UIDs nonzero
A new UID builds fresh gaze and distance history. Similar range alone cannot verify physical identity.
Notes: Appendix for questions.
All gates are required. Candidate must be newly acquired within 0.8s of old last sighting, exclusive throughout the gap, neither UID may be zero. Scalar distance allowance 0.25 +1.5*dt metres applies from old track and between candidate frames. At least three consistent frames span0.15s and have maximum gap0.35s. At most three rebinds per logical lock. Handoff retains lock ID, but the new raw track keeps its own epoch/fresh history. The handoff frame holds UID_REBOUND_OBSERVE. This is not the tracker nose continuity heuristic and not proof of personal identity.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/policy/target_lock.py
/Users/eddiekim/Documents/Projects/P4P/config/target-lock.json

## Slide 23
Policy Outputs, Locking and Execution
Appendix 16
23
Continuous rule command flow
Rule proposal
Target lock
Command planner
Opt-in execution
Selected-policy trial
Rules or LLM
Trial checks
First accepted action
Native action handler
The recorded evaluation ends at policy output. Acceptance is separate. Physical handlers require explicit execution.
Notes: Appendix for questions.
Do not depict the LLM as passing through rule correction or rule target locking. Continuous rule command flow uses pure proposal, target lock, command planner and opt-in execution feedback. Selected-policy SingleTrial uses the selected rules/LLM/VLM source directly, validates correlation/readiness/freshness and latches an accepted action. It does not reconsider a latched CONTINUE. Route settling precedes executing other actions when --single-trial-execute is enabled. Model audits outside selected trials are audit-only. This evaluation stops at first output and separately records acceptance; it instantiates no physical executor.
Sources:
/Users/eddiekim/Documents/Projects/P4P/docs/command-feedback.md
/Users/eddiekim/Documents/Projects/P4P/docs/robot-decision-dry-run.md
/Users/eddiekim/Documents/Projects/P4P/docs/live-model-inference.md
/Users/eddiekim/Documents/Projects/P4P/robot/navel_client/single_trial.py

## Slide 24
DecisionState v3: Included and Excluded Evidence
Appendix 17
24
Compact shared input | Full diagnostics or separate context
Readiness and empty-scene duration | Session/state IDs and timestamps
Robot motion category and description | Raw velocities and configuration
Current observed people | Missing-track lifecycle and events
Distance, gaze, trend and corridor categories | Raw head/nose geometry and fit statistics
Face evidence and descriptive labels | Detailed quality flags and provenance
Ten exact evidence operands | Cached rule settings outside observations
One canonical observation object for both policies
Notes: Appendix for questions.
DecisionState contains readiness, robot motion state/description, observed people in preserved order, distance/gaze/trend/face/corridor fields, semantic labels and ten exact numeric/validity rule operands. IDs and source timestamps are correlation context, not LLM text. Seven rule constants are cached separately. Full SocialState retains geometry, fit diagnostics, tracking history and configuration. Unsupported upstream measured path relation and pass gesture are removed throughout. Temporal summaries default NONE, preserving exact v3 JSON. Both production policy paths use the same canonical observation content.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/state/decision_models.py
/Users/eddiekim/Documents/Projects/P4P/docs/navel-supported-cues.md

## Slide 25
Readable Labels and Their Measurement Meaning
Appendix 18
25
Label | Meaning supplied to the LLM
Current gaze | Latest sample classified looking, not looking or unavailable
Attention over time | Recent little/no, intermittent or high-fraction looking
Proximity | Configured conversation/social-distance band
Relative separation | Robot-person distance getting closer, steady or farther
Corridor position | Current estimate inside, beside or behind the forward corridor
Face detection | Face detected, absent or unavailable
Either participant may change relative separation. Labels describe evidence without encoding an action or intention.
Notes: Appendix for questions.
Labels recompute from authoritative categories and validity. Current sample may be known before temporal gaze becomes usable. Invalid trend must be described as unavailable, not stationary. Distance categories are configured references, not willingness. Face detection does not establish facing. Labels contain no recommended action and do not establish intent, permission, predicted collision or clearance. These rows condense the exact English descriptions for readability; authoritative strings are in the state model.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/state/decision_models.py
/Users/eddiekim/Documents/Projects/P4P/app/policy/llm.py

## Slide 26
LLM Instructions and Output Validation
Appendix 19
26
Instruction guidance | Strict output checks
Use only supplied observed evidence | Exactly action and reason
Respect UNKNOWN and validity | CONTINUE / APPROACH / ENGAGE / YIELD
Separate history and current gaze | Nonblank reason string
Do not invent intent or permission | No extra fields
One concise sentence, at most 25 words | No semantic correctness or word-count check
{"action": "CONTINUE", "reason": "Observed evidence does not support interaction."}
Example output structure. Strict JSON validity and social appropriateness are separate measures.
Notes: Appendix for questions.
v16 asks for an independent judgement using compact measurements and the four action definitions. It distinguishes current gaze from history and high coverage fraction from uninterrupted looking, known absence from unavailable data, relative separation from individual motion and face detection from facing. No rule-based correction/fallback selects actions. Parser requires exactly action/reason, one of four enums, nonblank string and no extras. The <=25-word explanation is prompt guidance, not a semantic or length validator. All252 new stage7/8 calls are syntactically valid despite varying behavioural agreement.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/policy/llm.py
/Users/eddiekim/Documents/Projects/P4P/app/domain/model_decision.py
/Users/eddiekim/Documents/Projects/P4P/app/inference/ollama.py

## Slide 27
Input and Instruction Refinement Results
Appendix 20
27
Stage / arm | First alignment | Median delay | Input tokens | Decision
1-2 Full-state baseline | 6/9 | 6.21s | 1,766 | Reference
3 Compact state | 8/9 | 2.76s | 794 | Retain compact core
4 Semantic labels | 8/9 | 3.72s | 880 | Clearer meaning, no action gain
5 v14 on supported v3 | 8/9 | 3.31s | 842 | Fresh prompt control
5 Selected v16 | 8/9 | 3.04s | 917 | Retain instructions
6 Looking-change summary | 8/9 | 3.05s | 918 | Disabled
6 Detection-resumed summary | 8/9 | 3.06s | 917 | Disabled
Measured timings vary with runtime and cache. Stage 3 remains the faster historical 8/9 reference.
Notes: Appendix for questions.
Three warm operational repetitions per scored arm, same frozen first observations and allowed-action sets. Stages are separate sequential runs; timing is not a randomized causal estimate. Stage3 is fastest historical8/9 at2.76s. Stage4 adds meaning but has no action gain and costs time. Cue removal makes currentv3 but had no isolated model run. Stage5 uses a fresh v14/v3 control3.31s versus selectedv163.04s. Stage6 reuses that selected control; active first summaries do not improve8/9. No repeated-looking primary run occurs because its first inputs are unchanged.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-1-2/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-3/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-4/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-5/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-6/REPORT.md

## Slide 28
Temporal Summary Ablations: No First-Action Gain
Appendix 21
28
Summary | Active first cases | Primary score | Measured delay
Earlier looking, latest not looking | S4, S6, S7 | 8/9 | 3.05s
Repeated measured looking | None | No new primary trials | Not measured
Detection resumed after a gap | S7 | 8/9 | 3.06s
Why the additions stay disabled
No improvement in the frozen first actions
Extra text costs 36 to 37 tokens in affected inputs
Later diagnostic changes cannot repair the primary score
Notes: Appendix for questions.
Variants are independent. Looking change is justified by valid history, known latest classificationfalse and positive recent looking time. Repeated looking requires at least two measured bouts and does not assert episode durations. Detection resumed requires exact current REACQUIRED event matchingUID,epoch,timestamp. Reassociation/new acquisition/past events do not qualify. Events do not establish gaze during gap or a person physically returning. Positive summaries alone add fields and version4; inactive payload stays exactv3. DefaultNONE.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-6/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/docs/temporal-summary-experiments.md

## Slide 29
Inference Settings: Screen and Operational Check
Appendix 22
29
Direct screen | Context | Output cap | Median client call
Control | 8192 | 192 | 3.14s
Small context | 2048 | 192 | 2.99s
Small output ceiling | 8192 | 64 | 3.06s
Combined | 2048 | 64 | 3.00s
Operational arm | Alignment | Median | 95th percentile
Fresh control | 24/27 | 3.13s | 5.84s
Context 2048 | 24/27 | 3.07s | 5.91s
Only a 1.7% median gain with a slower tail. Retain context 8192 and output ceiling 192.
Notes: Appendix for questions.
Direct screens use one first snapshot call per scenario and are not primary operational scores. All retain8/9 actions and full prompttoken counts. Context2048 is fastest screen, hence selected for three operational repetitions against fresh control. The output64 ceiling cannot improve answers already terminating below64tokens. Confirmation gives3.13to3.07s (-1.7%) and p955.84to5.91 (+1.2%). Criteria require no scenario loss, all valid/untruncated output,>=10% median gain and no worsep95. Keep8192/192. Loaded memory falls4.98to4.62GB. Downloads overlap early settings blocks, limiting inference about a small difference.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/stage7/screen-selection.json

## Slide 30
Alternative Models: Accuracy and Timing
Appendix 23
30
Model | Each pass | Median | 95th pct. | Accepted | Aligned and accepted
Qwen 2.5 7B | 8/9 | 3.20s | 6.34s | 20/27 | 17/27
Qwen 3 4B Instruct | 7/9 | 2.49s | 4.46s | 24/27 | 18/27
Gemma 3 4B | 5/9 | 2.96s | 4.08s | 21/27 | 10/27
Qwen 2.5 3B | 4/9 | 1.81s | 3.12s | 22/27 | 12/27
Faster alternatives introduce more first-action mistakes
All first outputs are valid JSON. Acceptance and action agreement measure different things.
Notes: Appendix for questions.
All models use sharedv3/v16 text messages,temperature0 seed42 context8192 output192. Quantization/templates/tokenizers remainmodel-specific and /api/show metadata is saved. Three repetitions rotate model order and one model remains loaded at a time with warmweights. All27first outputs valid permodel. Qwen2.5 3B fixesS4butwronglyYieldsS1/S2/S6/S7/S9. Qwen3instructwronglyApproachesS1/S4 and claimsindividual motion/interest. Gemma3continuesallfirstcases. SelectQwen7B because no candidate preserves scenario quality. The experiment is M3,16GB,Ollama0.34.0;nohardwareactions.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/stage8/comparison.json

## Slide 31
All First Actions Across Models
Appendix 24
31
Case | Allowed | Rules | Qwen 7B | Qwen 3B | Qwen 3 4B | Gemma 4B
S1 | C | C | C | Y | A | C
S2 | A | A | A | Y | A | C
S3 | E / A | E | E | E | A | C
S4 | Y | Y | C | Y | A | C
S5 | C | C | C | C | C | C
S6 | C | C | C | Y | C | C
S7 | C | C | C | Y | C | C
S8 | A / E / C | C | C | C | C | C
S9 | A | A | A | Y | A | C
C = CONTINUE, A = APPROACH, E = ENGAGE, Y = YIELD. Every action repeats across all three passes.
Notes: Appendix for questions.
Every shown first action is stable across the three repetitions. C CONTINUE,A APPROACH,E ENGAGE,Y YIELD. S3 permitsE/A; S8permitsA/E/Cbecauseprimaryfirstdecisioncanoccurinempty scene. No model receives expected labels or scenario IDs as social evidence. Table showsnineunique cases,not27 independent encounters.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/config/final-scenarios.json

## Slide 32
Latency Components and Live Delivery
Appendix 25
32
Latest Qwen 7B measure | Value
Native prompt evaluation median | 1.88s
Native answer generation median | 1.27s
Native model-loading median | 0.003s
Eligibility to complete observed output | 3.20s median, 6.34s 95th percentile
Recorded motion to complete output | 4.31s median
Accepted / aligned and accepted | 20/27 / 17/27
Delivery check | Limit
Current observation age | 1s
Model source age | 10s
Trial deadline | 30s
Current readiness | Required
Correlation identity | Required
Medians of timing components do not add. Valid output can fail delivery as observations age or readiness changes.
Notes: Appendix for questions.
Baseline promptprocessing is77.35%of summed nativewarmtime,gen22.12,load0.09,other0.44. CurrentQwen7 first-request medians:prompt1.88s,gen1.27s,load0.003s. Do not add independently calculated medians to derive medianwalltime. latestcompleteobservedmedian3.20,p956.34. Firsteligibleaftermotionmedian1.166849,motiontooutputmedian4.307320,computed directly. Trialdeadline30s;currentobs<=1s,modelsource<=10s,ready/correlated. A continuinglive streamcanstayfreshafterclipend,whilecurrentreadinesscanstillchange. 20/27accepted;17/27bothalignedaccepted. NoLAN/hardwareexecution measurement.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-1-2/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/robot/navel_client/single_trial.py
/Users/eddiekim/Documents/Projects/P4P/scripts/profile_llm_baseline.py

## Slide 33
Final Pipeline Configuration for Live Trials
Appendix 26
33
Component | Retained selection
Shared observation state | DecisionState v3
Instructions | decision-state-llm-v16
Model | qwen2.5:7b
Generation | Temperature 0, seed 42
Context / output ceiling | 8192 / 192 tokens
Additional temporal summaries | NONE
Estimator / tracker | Final-scenario presets
Model condition | Preload with the same context before the encounter
Exact values: recommended-settings.json. Setup commands: docs/inference-settings-and-models.md.
Notes: Appendix for questions.
RetaincurrenttestedbaselinewithQwen2.5 7B,Statev3,Promptv16 andadditionaltemporalmodeNONE. Context8192,maxprediction192,temp0,seed42. Loadweightswithsamecontextbeforeencounterandkeepintendedmodelresident. Measurementsalreadyassumewarmweights;preloadisreproductionconditionnotclaimedextra gain. Effective temporal/tracking finalpresets remainexplicit. HTTPtimeout120s is transportlimit,separatefrom30sSingleTrialdeadline. Actualv16messagesandstatehashesverified. Originalcopiedprotocolsettingspromptversionmetadataisunusedhistoricalv14;recommended-settings.jsoncorrectsv16metadata.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/recommended-settings.json
/Users/eddiekim/Documents/Projects/P4P/docs/inference-settings-and-models.md
/Users/eddiekim/Documents/Projects/P4P/app/state/decision_models.py

## Slide 34
Research Findings and Remaining Limits
Appendix 27
34
Research finding | Evidence boundary
Shared state supports policy comparison | Same inputs; rules unchanged across 574 frames
Compact input improves action match and delay | 6/9 to 8/9; roughly half the initial delay
Rules lead on these tuning cases | 9/9 expected first actions versus 8/9 LLM
Extra temporal descriptions add no gain | No improvement in expected first actions
Direct human alignment remains incomplete | Verify survey reference and endpoint mapping
Physical execution needs separate evidence | Recorded replay and scripted demos differ
Sources and exact values appear in each slide’s speaker notes. Main presentation ends at slide 7.
Notes: Appendix for questions.
RQ1: implementedcausalsharedevidencewithhistory,validityandcompactinput;all574framespreservetunedruledecisions/readiness,402eligible. RQ2:currentfirst-actioncomparisonfavoursrules,whileformalhumanpreferencealignmentneedssurveyendpointmappingandfinalverifiedworkbook. Do notclaim9/9humanagreement. Nine recordings are tuning cases,notheldoutaccuracy. Deterministicrepeatsmeasurestabilitynotindependent sample size. SourceS8firstemptyandS6firstbeforelaterglance;do notinferlatercueunderstanding. Corridorfixedheadproxyandreassociationidentityheuristicsneedindependentvalidation. Replayendsatoutput,notphysicalexecution. Historicalstage3at2.76sremainfastest8/9observedrun;finalpipeline3.0to3.2snotprovenbetterbecauseofricherlabels.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/REPORT.md
/Users/eddiekim/Documents/Projects/P4P/docs/pipeline-refinement.md
/Users/eddiekim/Documents/Projects/P4P/docs/llm-refinement-summary.md

## Slide 35
Model Trade-Off: Earlier Answers and Action Agreement
Appendix 28
35
Chart: Aligned scenarios out of 9
| 3.198938208357364
Qwen 2.5 7B | 8
Qwen 3 4B Instruct | 7
Gemma 3 4B | 5
Qwen 2.5 3B | 4
Accuracy first
Retain the 7B model:
8/9 expected first actions
at a median 3.20s.
Fastest tested model:
4/9 at 1.81s.
Every point uses identical shared observation messages and v16 instructions.
Notes: Appendix for questions.
This editable scatter plot uses the same fresh model comparison. Each point is one model, with median first-output delay and number of aligned unique scenarios. All three repeats yield the same counts. Faster models do not preserve the 7B baseline action agreement. This is a nine-scenario tuning comparison on an Apple M3 with 16GB, not a general benchmark. Model inference times include the local complete-output path.
Sources:
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/REPORT.md

## Slide 36
Exact Compact Evidence Operands
Appendix 29
36
Exact operand | S4 first value | Meaning
gaze_valid | true | Temporal gaze sufficiency
distance_trend_valid | true | Trust fitted separation trend
latest_distance_valid | true | Use current measured distance
latest_gaze_looking | false | Current hysteresis classification
latest_gaze_overlap | 0.8352 | Current measured gaze score
looking_exit_threshold | 0.9500 | Effective sample exit threshold
looking_bouts | 1 | Measured looking episode count
looking_time_s | 0.0853 | Covered looking duration
gaze_fraction | 0.1229 | Looking time / covered time
sustained_gaze_s | 0 | Trailing continuous looking run
Displayed values are rounded. Model input preserves exact numeric operands and validity flags.
Notes: Appendix for questions.
These ten fields retain all numeric/validity operands required by the tuned rules. The compact object also contains current distance/categories, face/corridor observations and semantic descriptions, as shown earlier. Values here are the actual first S4 snapshot and rounded only for display. The policy and model JSON preserve full precision. Neither source IDs nor raw geometry enter LLM text. Looking exit remains because a false sample in the hysteresis band does not necessarily satisfy the rule low-score YIELD condition.
Sources:
/Users/eddiekim/Documents/Projects/P4P/app/state/decision_models.py
/Users/eddiekim/Documents/Projects/P4P/var/evaluation/llm-refinement-stage-7-8/common/snapshots/S4/first.decision-state.json